## Slide 2: Welcome
David Solsrud

## Slide 3: Introductions
Name
Office
Involvement With AMSIP or Asset Management
What Do You Want To Get Out of The Workshop?
You Get 30 Seconds!
Notes: Make sure someone is recording these and bring them up throughout the workshop and at the end.

## Slide 4: Workshop Team
Dave Solsrud, Manager - Asset Management Program Office
Trisha Stefanski, Asset Engineer – AMPO/Metro District
Michael Cremin, Project Engineer – AMPO
Mitch Webster, Planning– OTSM/Maintenance
Katie Zimmerman, AP Tech
Brad Allen, AP Tech
Bill Roberts, Spy Pond Partners

## Slide 5: Today’s Objectives
Engaging, Interactive, & Fun Workshop
Learn About AMSIP and The Asset Matrix
Better Understand The Matrix Building Process
Walk The Walk-Through Results
  AM Approaches
  Tiers
  Return on Investment Analysis
  Asset Data and Costs
“Get Down To Brass Tacks”, Details of Immediate Practical Importance.
Set The Stage For AMSIP Roadmap
Notes: Virtual format challenges
Leverage you precious time once… thanks for agreeing. Time is short, bandwidth is limited, and I promised this would be a collaborative process
Lots of work done behind the scenes – even matrix team unaware
My goals: make as many decisions as we can – minimize further study/research. These are management decisions rely on judgements in addition to data. We have tried to bring as much data as we can forward. Need to keep the momentum, bring to closure.
“Approaches, Tiers” to help categorically decide
Trish, Mike, Mitch. No one collectively knows more about what is going on with our data, and options, costs, uses. Rather than pose questions to this group – (70+ assets) I asked for recommendations
Talk about data uses, data costs ($, staff labor) concerns expressed re cost, also hard to quantify benefits.
We looked for reductions as well as add’s. Lot’s of “stay the course”, lots of adds, not so many reductions in data, but savings in process opportunities. Internal vs Consultant resources
My 3 nuances:
A lot is already being done both acquiring/maintaining data, but also use
Think future: Technology is advancing rapidly – Satellite imagery, Iphone surveys, Opensource data – it’s ok to stretch ourselves at this point
Crowd source data use – uses have greatly exceeded the initial intent of lots of our data collection (restitution, 081 funding, scoping, sign design plans) What else? TSMO? CAV?

## Slide 6: Incedentally…
Asset Data Analytical Needs/Capabilities

## Slide 7: Agenda
1:15 | Asset Management Strategic Implementation Plan
1:30 | Building The Matrix
2:00 | Return on Investment Analysis
2:15 | 15 Minute Break
2:30 | Results
3:30 | Recommendations
4:00 | Round Robin
4:15 | Wrap Up, Next Steps
*Trivia, Polling, and Q&A Chat Sprinkled Throughout The Workshop | 
Notes: Katie

## Slide 8: Asset Management Strategic Implementation Plan
Notes: Overview of plan

## Slide 9: Benefits of Asset Management
Improved asset condition, performance, resilience, and longevity.
Increased efficiency and effectiveness. Regular maintenance can be planned and scheduled, reducing disruption to service as little as possible.
More benefit for each dollar invested. TAM helps to ensure that the benefits delivered by the network are maximized, while the costs of providing, maintaining, and using it are minimized.
Reduced risk exposure. When assets are maintained and managed consistently and resilience is improved, the agency reduces the exposure to risk.
Improved coordination and communication. Asset management helps potential silos within an agency by improving resource allocation and improving coordination between staff on asset management related projects and maintenance
Major Rehab
PM
Reactive
Maint.
Reactive
Maint.
Reactive
Maint.
LIFE OF ASSET
PM
Installation
Notes: Katie?

## Slide 10: Strategic and Mature Asset Management
Notes: Katie?

## Slide 11: AMSIP Background
Map-21
  Requires states to prepare Transportation Asset Management Plans (TAMP)
  Also requires action “implementation”
TAMP Implementation Workshop
  April 2019
  Valuable Feedback
Mn State Statute 174.03
  “The Commissioner must maintain an inventory of transportation asset, including but not limited to bridge, pavement, geotechnical, pedestrian, bicycle, and transit asset categories.”
Notes: katie

## Slide 12: TAMP Implementation Workshop Feedback
TAMP Assets
Asset Demands on District Staff
Data Roles, Responsibilities
Preventive Maintenance Barriers
Maintenance Funding
TAMP and MnSHIP Integration
Data Needs Beyond AM,
  For example, 081, Restitution, Scoping, Design
Long Range Goals & Measures
Decision Making Constraints
Notes: katie

## Slide 13: AMSIP Planning Initiatives and Outcomes
Strategic – How Far Are We Going?
  MnDOT Strategic Operating Plan  Tangible
  Shared Vision  Documented
Implementation – People, Process, Data
  Roles and Responsibilities
  Process/Practices
  Data Acquisition and Maintenance
  Emphasis on Actionable and Tangible Outcomes
  Maximize Number of Decision Made During Planning Effort
  Emphasis On Collaborative Plan Development
Notes: katie
Again – focus on maximizing decision making today

## Slide 14: AMSIP “High 5” Technical Working Teams
Asset Matrix “Team Matrix” – Trisha Stefanski & Brad Allen
Geotechnical Assets – Brad Skow & Bill Roberts
Preventive Maintenance – Glenn Engstrom & Brad Allen
Communication Plans and Execution – J.T. Anderson & Katie Zimmerman
TAMP Topics – Shannon Foss & Katie Zimmerman
Notes: katie

## Slide 15: Building The Asset Matrix
Trisha Stefanski, PE - Mndot
Brad Allen, PE – Applied Pavement
Notes: Brad and Trish

## Slide 16: Team Matrix
Objective – Use National Best Practices To Categorize Assets Classes Into Priority Tiers and Clarify (1) How Assets and Asset Data Is Managed (2) The Data Needed To Support The Management, and (3) Roles and Responsibilities
Leadership Team – Brad Allen, Katie Zimmerman, Dave Solsrud, Trisha Stefanski, Michael Cremin, Mitch Webster
Team Members - Michael Barnes, Perry Collins, Paul Czech, Michael Ginnaty, Jay Hietpas, Susan Karnowski, William Pirkl, Mark Schoenfelder, Todd Stevens, Brad Utecht.
Notes: brad

## Slide 17: District Survey Asset Importance, Data Availability, Score
Notes: Brad

## Slide 18: Development Of The Asset Matrix
Asset Responsibilities Database
Asset Classes
Asset Data Needs
Asset Tiers
Asset Management Approaches
Asset Drivers
Data Collection Methodology
Partner w/Geotechnical TWT
Return on Investment
Partner w/TAMP TWT
Data Collection Plan
Working Matrix
Notes: brad

## Slide 19: Asset Management Approach
How Are We Currently Managing Our Assets?
What Is Our Desired Asset Management Approach?
Question | Minimum Maintenance | Reactive | Cycle Driven | Cycle Driven + | Condition Driven | Condition Driven +
Require Asset Inventory? |  | X | X | X | X | X
Require Asset Maintenance Cycle? |  |  | X | X | X | X
Require Asset Condition Data? |  |  |  | X | X | X
Require Long-Term Performance Mgmt? |  |  |  |  | X | X
Optimizing Life Cycle? |  |  |  |  |  | X
Notes: Trish – this is a way of consolidating data related decisions

## Slide 20: Asset Management Approach
Approach | Definition | Inventory Data | Condition Data | Management Demand
Condition Driven Plus | The condition of the asset is routinely monitored and modeled. Actions are taken proactively and reactively to optimize the asset lifecycle through minimum lifecycle cost, maximum benefit, maximum life-cycle length, or some similar approach | Yes | Yes | Highest
Condition driven | The condition of the asset is routinely monitored, and actions are taken to manage the long-term performance of the asset or the assets impact on system performance. | Yes | Yes | High
Cycle Driven Plus | The asset is inspected and maintained on a cyclical basis, where the inspection and maintenance activities are performed in simultaneously or in concert and condition data is collected and maintained for analysis | Yes | Yes | Med-high
Cycle Driven | The asset is maintained on a cyclical basis. Condition data may be collected on these assets to meet other business needs but the inspection cycle is managed separately from the maintenance cycle. | Yes | No | Med
Reactive | An inventory is maintained, but there is no regular condition data collection, and no maintenance performed to slow or address damage or deterioration until an asset is reported as having an unacceptable defect. Annual work is planned at the aggregate level, without concern for the specific locations of potential future defects. | Yes | No | Med-low
Min Maintenance | No inventory or condition data is collected or maintained. Maintenance is performed when assets are identified as having an unacceptable defect. | No | No | Low

## Slide 21: Asset Drivers
Number of Assets
Value of Assets
Mandates, Regulation, Policies
Risk and Risk Mitigation
Number of Data Consumers
Portion of MnSHIP Investment Allocation
Portion of Ops Budget Allocation
TAMP Asset

## Slide 22: Asset Tiers
Tier 1 assets represent a combination of the highest monetary valued assets along with assets that are critical to public safety, mobility, and the economy. Failure of a single asset could lead to an immediate safety risk or impact the transportation network for an entire region Poor performance by a group of similar assets could result in regional or even statewide impacts. As a result, these assets receive the greatest level of scrutiny and resources dedicated to inventory and condition data collection, investment decision making, maintenance, and capital investments to provide the highest practical level of service and reliability.
Notes: See reference doc from michael
May need to clarify how tiers and approaches complement each other

## Slide 23: Asset Tiers
Tier 2 assets are typically not as high-value as tier 1 assets, but still represent a significant consequence to public safety upon failure for a corridor or municipality. As a result, MnDOT dedicates resources to pro-actively monitoring and subsequent interventions to prevent unacceptable performance. The agency collects and uses inventory and condition data on these assets to identify, prioritize, and deliver maintenance and repair actions to cost-effectively manage the assets throughout their service lives.

## Slide 24: Asset Tiers
Tier 3 assets support safety and system performance at their specific locations. Individual failures of these assets can have significant local impacts but are of limited consequence to overall network performance. These assets typically benefit from routine or cyclical replacements, of components or whole assets, to ensure proper performance. Inventory data is collected to support the efficient scheduling and delivery of appropriate cyclical work. Additionally, condition data may be collected for some assets to comply with mandates (e.g., municipal separate storm sewer systems), optimize the maintenance and replacement cycles (e.g. sign panels), or both.

## Slide 25: Asset Tiers
Tier 4 assets represent limited risk to the transportation network. Failure of these assets generally impacts only the location served by that asset. To mitigate these risks, MnDOT has guidelines regarding maintenance response times to repair or replace assets within a certain period after being notified of the unacceptable condition to minimize the impact on safety and system performance. MnDOT collects and routinely updates inventory on these assets but doesn’t collect condition data, to ensure the agency has an accurate accounting of the current infrastructure and its needs. Work performed to maintain, improve, or replace these assets is tracked, specific to each individual asset or installation

## Slide 26: Baseline Data Inventory
Specialty Office Meetings/AMPO Knowledge
  Full/Partial/None
  Collection Needs to Complete Baseline
  Baseline Inventory Data
  Current Resource Allocated
  Desired Resource Add
  How
  Who
  One-time Cost Estimate
  Timeline
Baseline Method Description
Utilize Design Data
Field Walks
Mobile Imagery
Mobile LiDAR
Internal Knowledge (MnDOT Crowd Sourcing)
Satellite

## Slide 27: Data Inventory Currency
Currency Method ID | Currency Method Description
A | SRC As-Builts
B | Utilize Design Data & As-Builts
C | Utilize Design Data & Construction As-Builts & Annual LiDAR Survey
D | Annual Imagery*
E | MnDOT Forces During Construction projects
F | AVL and/or Data Logging System
G | Linear Referencing Systems
 | * Maplewood Van Option
Specialty Office Meetings/AMPO Knowledge
  7 Methods
    Current, Possible, Preferred, No
  Current Resource Allocated
  Desired Resource Add
  Annual Cost Estimate
    # of Asset
    % Change upon life cycle
    Applied Unit Cost

## Slide 28: Data Inspections Condition or Assessment Data
Inspection Method ID | Inspection Method Description
H | Visual Inspection (VT)
I | Physical Field Device Inspection
J | MnDOT Pavement Van Sensors
K | Satellite or Aerial Imagery
L | Drone Inspection
M | Mobile Lidar
Specialty Office Meetings/AMPO Knowledge
  Refer to AM Approach to Determine Desired Inspection Requirement
  6 Methods
    Current, Possible, Preferred, No
  Current Resource Allocated
  Desired Resource Add
  Annual Cost Estimate
    No. of Asset Units
    No. of Inspections
    Inspection Cost/Unit
    Inspection Frequency
    Total Cost

## Slide 29: Other Data Implementation Tasks
Task Descriptions
  Software Upgrades or Enhancements
  Training Opportunities
  Level of Detail Within Asset Inventories
  Current Research Projects
  Business Process Changes or Documentation
    Design
    Inspection Guides
    Inspection Frequency
Short-term or Long-term
Roles and Responsibilities TBD
Notes: Some already happening
Will be part of roadmap

## Slide 30: Return On Investment Analysis
Bill Robert, spy pond partners

## Slide 31: Return On Investment (ROI) Analysis
Performed this analysis to better quantify the benefits of collecting additional data for selected asset types
Focused specifically on calculating the ROI of adding more culverts to the inventory (side and entrance culverts)
Used framework and tool from NCHRP Report 866
Performed calculations for a representative district
Reviewed the framework and tool in a web-based workshop, then followed up with District 2 staff for more data

## Slide 32: NCHRP Report 866 Contents
Framework addressing evaluation of ROI and other financial metrics for asset management system/process investments
Set of case studies illustrating calculation of ROI and demonstrating potential benefits of asset management system/process investments
Guidance document and tool with step-by-step procedures agencies can follow to calculate ROI and other metrics for a proposed asset management system/process investment

## Slide 33: ROI Calculation Steps
Plan
1. Define Purpose of Study and Scope of TAM Investment
2. Identify Likely Impacts
Collect
4. Establish Modeling Approach and Identify Tools
Analyze
6. Conduct Analysis
7. Estimate ROI and Summarize Results
3. Assess Available Data
5. Collect Necessary Data

## Slide 34: MnDOT ROI Analysis Participants
Initial Workshop – 11/12
  Ruth Betcher
  Tara Carson
  Andrea Hendrickson
  Kris Langlie
  Doug Maki
  Greg Masteller
  Bridget Miller
  Rachel Miller
  David Mohar
  Scott Morgan
  Beth Neuendorf
  Lisa Sayler
  Allen Schmitz
  David Solsrud
  Jason Swenson
  Trisha Stefanski
  Kellie Thom
Follow-Up Discussion – 12/9
  Ruth Betcher
  Michael Cremin
  Andrea Hendrickson
  Lisa Sayler
  Josh Stearns
  Kellie Thom
  Mitch Webster

## Slide 35: Culvert Analysis
Costs of Additional Culvert Data (per district)
  Startup/Training – 80 intern hours
  Plan Review – 600 intern hours
  QA/QC – 40 MnDOT staff hours
  Field Work – 2,160 MNDOT staff hours (27 weeks x 2 people)
  Intern = $72,000/year
  MnDOT Staff = $150,000/year

## Slide 36: Culvert Analysis (continued)
Benefit of Additional Data (per district)
  Reduced time for field review
    120 intern hours per year
    240 MnDOT staff hours per year
  Reduced time to respond to issues/incidents
    80 MnDOT staff hours per year (10 issues x 8 hours per issue)
  Reduced downtime as a result of culvert failures
    1 incident/year
    Reduction in closure of 1 week
    Assumed closure requires detour of 100 vehicles/day by 0.1 mile at 5 mph
    $372 detour costs reduced/year
  Other more difficult-to-quantify benefits include assisting in spill prevention, improving maintenance efficiency…

## Slide 37: Culvert ROI Calculations
Net benefits
  Agency: $20K
  User/Social: $3K
ROI measures
  NPV: $23K
  IRR: 6.74%
  Payback Period: 7 years

## Slide 38: Conclusions
It is feasible to quantify an ROI for TAM data improvements
Return is positive for collecting additional culvert data
Many types of potential benefits from TAM improvements
  Agency cost savings
  Reduced impacts to users
  Reduced environmental impacts
  Improved investment outcomes (very large where applicable)
Some of the benefits are qualitative or difficult to quantify – a description of these should complement and ROI calculations

## Slide 39: Trivia Time
Please go to menti.com CODE ZZZZ

## Slide 40: Results
Trisha Stefanski, pe
15-minute break
Start back at

## Slide 41: Asset Groups and Asset Classes
Bike and Ped | Accessible On-street ADA Parking
Bike and Ped | Pedestrian curb ramps, signals, and sidewalks
Bike and Ped | Bike Lane (not sep) and shared roadways
Bike and Ped | Shared use paths, side paths, separated bike lanes
Bridges | Vehicle Bridges >10' and Tunnels
Bridges | Bridge Pedestrian/Bicycle/Utility
Bridges | Bridge Clearance
Facilities | Class 1 Rest Areas, Class 1 Truck Stations, Office Buildings, Salt Sheds (S&I Operations)
Facilities | Class 2 and 3 rest areas, class 2 and 3 Truck Stations, Brine Buildings (S&I Operations), Weigh Stations
Facilities | Storage sheds, and misc. buildings (lift stations, hazmat, etc.)
Facilities | Class 4 rest areas
Geotechnical | Earth Retaining Systems (includes gravity, soil nail, soldier pile, sheet pile, reinforced concrete cantilever, MSE, crib, bin, timber, other types on the TAMS list)
Geotechnical | Reinforced Soil Slopes
Geotechnical | Improved Ground Supports (includes column-support embankments and transfer platforms)
Geotechnical | Instrumentation Systems (includes inclinometer, pressure cell, gauge, cabinet, and piezometer)
Geotechnical | Special Drainage Systems (includes chimney drain, perforated drain, herringbone drain, geomembrane cap and liner, and trench drain - does not include edge drains)
Geotechnical | Natural Hazard Locations (includes locations off of the ROW not otherwise addressed)
Geotechnical | Improved Subgrade Fills (includes lightweight fill such as: wood chip, tire-derived aggregate, geofoam, lightweight aggregate, cellular concrete, and grouted fill)
Geotechnical | Unimproved Subgrade
Geotechnical | Cut Slopes
Geotechnical | Embankments
Green Assets | Hazard - Noxious Weeds
Green Assets | Replacement Wetlands
Green Assets | Trees (Types: Historic, Notable, High-Risk, Land Bearing)
Green Assets | Native/Pollinator Plantings
Green Assets | Landscaping
Green Assets | Roadway Ditches
Hydraulic Infra | Highway Culverts
Hydraulic Infra | Deep Stormwater Tunnels
Hydraulic Infra | Ponds, Infiltration Basins, and Underground Storage
Hydraulic Infra | Storm Sewer Pipe and Structures
Hydraulic Infra | Structual Pollution Control Devices (SPCD's)
Hydraulic Infra | Local Road Culverts
Hydraulic Infra | Entrance Culverts
Maintenance | Snow and Ice Winter Plow Route
Maintenance | Stationary Anti-Icing Systems
Maintenance | Roadway Weather Information System (RWIS)
Maintenance | Snow Fence (Types: Living, Structural, Grading)
Maintenance | Mowing
Maintenance | Debris Removal
Notes: Started with AM Responsibility effort from 3 years ago

## Slide 42: Assets
Pavements | Highway Mainline
Pavements | High Volume Frontage Roadway
Pavements | Bus Shoulders
Pavements | Highway Ramps/loops
Pavements | Paved Shoulders
Pavements | Low Volume Frontage Roads
Pavements | Edge Drains
Pavements | Drain Tile
Pavements | Curb and Gutter
Pavements | Gravel Shoulders
Rail | Rail/Rail Crossings (non-MnDOT maintenance responsiblities)
Right of Way | Land, Boundary, Excess or Surplus Right of Way
Right of Way | Fence
Structures | ARMER System - radio towers, equipment shelters, radio transmission equipment, facilities
Structures | Wood Noisewalls
Structures | Entrance Monuments
Structures | Concrete Noise
Structures | Billboards (Permit Requirements only)
Traffic | Freeway Management Systems (TMS, RTMC operations, ITS)
Traffic | Signal Systems
Traffic | Lighting - High Mast Towers
Traffic | Sign Panels - Static
Traffic | Sign Structures - Static Panel Ground Mounted
Traffic | Sign Structures - Static Panel Overheads w/Foundations
Traffic | Sign Structures - I-beam w/Static Panel
Traffic | Lighting - Roadway
Traffic | Barrier - Attenuators (Crash Cushions)
Traffic | Barrier - Plate beam End treatments
Traffic | High Tension Cable Barrier
Traffic | Barrier - Plate beam
Traffic | Pavement Markings - Messages
Traffic | Pavement Markings - Striping
Traffic | Concrete Barrier
Traffic | Rumble Strips and Stripes
Notes: 78 Asset

## Slide 43: Matrix Spreadsheet
Overview of Matrix Spreadsheet
  Matrix Tier Drivers
  Inventory Baseline Plan
  Inventory Currency Plan
  Inspection Plan
  Implementation Tasks
  Strategic Plans Summary
Demo Time

## Slide 44: The “Didn’t Make the Tier” Assets
Key Takeaways
  No Inventory
  No Inspection
  Reduce Any Data Collection Efforts
 | Matrix Drivers |  |  |  |  | 
Asset ID | Asset Group | Asset Class | Tier | Desired AM Approach | AM Maturity Step Gap | 
61 | Hydraulic Infra | Entrance Culverts | 5 | Reactive | 1 | 
60 | Green Assets | Landscaping | 5 | Other | 0 | 
62 | Maintenance | Mowing | 5 | Other | 0 | 
63 | Maintenance | Debris Removal | 5 | Other | 0 | 
73 | Rail | Rail/Rail Crossings (non-MnDOT maintenance responsiblities) | 5 | Other | 0 | 
74 | Structures | Billboards (Permit Requirements only) | 5 | Other | 0 | 
75 | Bridges | Bridge Clearance | 5 | None | 0 | 
69 | Geotechnical | Unimproved Subgrade | 5 | Min. Maint. | 0 | 
70 | Geotechnical | Cut Slopes | 5 | Min. Maint. | 0 | 
72 | Geotechnical | Embankments | 5 | Min. Maint. | 0 | 
66 | Green Assets | Roadway Ditches | 5 | Min. Maint. | 0 | 
64 | Pavements | Edge Drains | 5 | Min. Maint. | 0 | 
67 | Pavements | Drain Tile | 5 | Min. Maint. | 0 | 
68 | Pavements | Curb and Gutter | 5 | Min. Maint. | 0 | 
65 | Right of Way | Fence | 5 | Min. Maint. | 0 | 
71 | Pavements | Gravel Shoulders | 5 | Min. Maint. | 0 | 
Notes: Entrance culverts reactive

## Slide 45: Tier 1 Asset Results
 | Matrix Drivers |  |  |  |  | 
Asset ID | Asset Group | Asset Class | Tier | Desired AM Approach | AM Maturity Step Gap | 
1 | Bridges | Vehicle Bridges >10' and Tunnels | 1 | Condition+ | 0 | 
4 | Facilities | Class 1 Rest Areas, Class 1 Truck Stations, Office Buildings, Salt Sheds (S&I Operations) | 1 | Condition+ | 0 | 
2 | Pavements | Highway Mainline | 1 | Condition+ | 0 | 
5 | Structures | ARMER System - radio towers, equipment shelters, radio transmission equipment, facilities | 1 | Cycle+ | 0 | 
6 | Traffic | Freeway Management Systems (TMS, RTMC operations, ITS) | 1 | Cycle+ | 0 | 
7 | Traffic | Signal Systems | 1 | Cycle+ | 0 | 
3 | Maintenance | Snow and Ice Winter Plow Route | 1 | Other | 0 | 
High Network Risk
Modeling
Condition +
Cycle +
High Maturity

## Slide 46: Tier 1 Asset Results
 | Matrix Drivers |  |  |  |  |  |  |  | Plan summary |  | Baseline Inventory |  | Inv. Currency | Condition Inventory |  | System standup |  |  | 
Asset ID | Asset Group | Asset Class | Asset Class | Tier | Tier | Desired AM Approach | AM Maturity Step Gap | AM Maturity Step Gap | Short Description | 5 year Plan Sub-total ($10k resolution) | Timeline To Complete Inventory | Inventory Baseline Cost Estimate | Inventory Currency Annual Cost Estimate | Timeline To Complete Inspection Cycle | Inspection Plan - Annual Cost Estimate (Baseline incl.) | Other Imp. Tasks | Strategic Asset Unit | Statewide Count | 
1 | Bridges | Vehicle Bridges >10' and Tunnels | Vehicle Bridges >10' and Tunnels | 1 | 1 | Condition+ | 0 | 0 | Stay the course | Calc pending | NA | Calc pending | $10,000 | NA | $2,300,000 | 0 | Bridges | 4,599 | 
4 | Facilities | Class 1 Rest Areas, Class 1 Truck Stations, Office Buildings, Salt Sheds (S&I Operations) | Class 1 Rest Areas, Class 1 Truck Stations, Office Buildings, Salt Sheds (S&I Operations) | 1 | 1 | Condition+ | 0 | 0 | Stay the course | Calc pending | NA | Calc pending | Calc pending | NA | $400,000 | 0 | Building Sites | 600 | 
2 | Pavements | Highway Mainline | Highway Mainline | 1 | 1 | Condition+ | 0 | 0 | Stay the course | $6,810,000 | NA | $ - | $72,000 | NA | $2,150,000 | 1 | Centerline miles | 14,331 | 
5 | Structures | ARMER System - radio towers, equipment shelters, radio transmission equipment, facilities | ARMER System - radio towers, equipment shelters, radio transmission equipment, facilities | 1 | 1 | Cycle+ | 0 | 0 | Stay the course | Calc pending | NA | Calc pending | Calc pending | NA | $70,000 | 0 | Systems | 350 | 
6 | Traffic | Freeway Management Systems (TMS, RTMC operations, ITS) | Freeway Management Systems (TMS, RTMC operations, ITS) | 1 | 1 | Cycle+ | 0 | 0 | Stay the course | Calc pending | NA | Calc pending | Calc pending | NA | $572,000 | 0 | Systems | 14,310 | 
7 | Traffic | Signal Systems | Signal Systems | 1 | 1 | Cycle+ | 0 | 0 | Stay the course | Calc pending | NA | $ 38,000 | Calc pending | NA | $750,000 | 6 | Systems | 1,500 | 
3 | Maintenance | Snow and Ice Winter Plow Route | Snow and Ice Winter Plow Route | 1 | 1 | Other | 0 | 0 | Stay the course | $310,000 | NA | $ - | $1,000 | NA | $100,000 | 0 | TAMS Sections | 500 | 
Total | Totals |  |  |  |  |  |  |  |  | $ 7,120,000 |  | $38,000 | $83,000 |  | $6,342,000 | 7 |  |  | 
Notes:   Discuss Plan summary = total costs over 5 years – sticker shock
  Baseline Inventory - Inventories Complete, Active: Signal Pole Locations From LiDAR
  Inventory Currency - Design Plans/As-Builts
  Inspection Processes – Robust, Active: Are Bridge Crews Inspecting Signals, Active: Perform ADA Site Assessments on rest areas and other MnDOT owned facilities.
  Other Implementation Items
    IT Project Request for HPMA Replacement
    Transportation Research Synthesis On Preventive Maintenance/Inspection Signals (and OSS, lighting).
    TAMS 3 Integration with S&I MDSS
    Development of preventive maintenance standards, cycles, and Archibus triggers for select facilities equipment. This will include additional attribution within Archibus for the Districts

## Slide 47: Tier 1 Asset Data Collection Plan
Fun Fact: Tier 1 Assets are Managed in 6 Unique Enterprise Asset Management Systems
47
“We started adding ITS cabinet equipment so we can automatically pull asset info like serial#, firmware, make, model etc. We are trying to leverage automation, so hand entry is needed less.”
“AMER inspections occur on 3-year cycle for guide wires and towers via TIA requirements, quarterly inspection required by FAA (remote alarm system but verify once per quarter). Five-year for fixed tower and look over the site as well”.
“We are advancing deterioration modeling for all bridge and culvert elements”
“The future integration of MDSS Data and TAMS for Snow and Ice recording will reduce data entry into RCA”.
Stay The Course

## Slide 48: Tier 2 Asset Results
  Tier 2
    Not as High Value
    Significant Consequence
    Proactive Monitoring
  Asset Groups
    Bike and Ped
    Geotechnical
    Mainline Culverts
    Geotechnical
    Ancillary Pavements
    High Mast
  Condition, Cycle+
  Maturity Gaps
 | Matrix Drivers |  |  |  |  | 
Asset ID | Asset Group | Asset Class | Tier | Desired AM Approach | AM Maturity Step Gap | 
11 | Bike and Ped | Pedestrian curb ramps, signals, and sidewalks | 2 | Condition | 4 | 
10 | Bike and Ped | Accessible On-street ADA Parking | 2 | Condition | 4 | 
12 | Bike and Ped | Bike Lane (not sep) and shared roadways | 2 | Condition | 4 | 
9 | Bridges | Bridge Pedestrian/Bicycle/Utility | 2 | Condition | 0 | 
19 | Geotechnical | Earth Retaining Systems (includes gravity, soil nail, soldier pile, sheet pile, reinforced concrete cantilever, MSE, crib, bin, timber, other types on the TAMS list) | 2 | Condition | 4 | 
20 | Geotechnical | Reinforced Soil Slopes | 2 | Condition | 4 | 
21 | Geotechnical | Improved Ground Supports (includes column-support embankments and transfer platforms) | 2 | Condition | 4 | 
8 | Hydraulic Infra | Highway Culverts | 2 | Condition | 0 | 
22 | Maintenance | Stationary Anti-Icing Systems | 2 | Cycle+ | 0 | 
17 | Pavements | Bus Shoulders | 2 | Cycle+ | 2 | 
16 | Pavements | High Volume Frontage Roadway | 2 | Cycle+ | 2 | 
18 | Pavements | Highway Ramps/loops | 2 | Cycle+ | 2 | 
23 | Traffic | Lighting - High Mast Towers | 2 | Cycle+ | 0 | 

## Slide 49: Tier 2 Asset Results
(Stay the Course Spreadsheet)
Notes: Stay The Course

## Slide 50: Tier 2 Asset Results
 | Matrix Drivers |  |  |  |  |  |  |  | Plan summary |  |  | Baseline Inventory |  |  | Inv. Currency | Condition Inventory |  |  | System standup |  |  |  |  | 
Asset ID | Asset Group | Asset Class | Asset Class | Tier | Tier | Desired AM Approach | AM Maturity Step Gap | AM Maturity Step Gap | Short Description | 5 year Plan Sub-total ($10k resolution) | 5-year Plan Sub-total ($10k resolution) | Timeline To Complete Inventory | Inventory Baseline Cost Estimate | Inventory Baseline Cost Estimate | Inventory Currency Annual Cost Estimate | Timeline To Complete Inspection Cycle | Inspection Plan - Annual Cost Estimate (Baseline incl.) | Inspection Plan - Annual Cost Estimate (Baseline incl.) | Other Imp. Tasks | Strategic Asset Unit | Strategic Asset Unit | Statewide Count | Statewide Count | 
10 | Bike and Ped | Accessible On-street ADA Parking | Accessible On-street ADA Parking | 2 | 2 | Condition | 4 | 4 | Add | $ 20,000 | $20,000 | <1 year | $ 3,000 | $3,000 | $1,000 | 3 to 5 years | $ 4,000 | $4,000 | 3 | Spots | Spots | 200 | 200 | 
12 | Bike and Ped | Bike Lane (not sep) and shared roadways | Bike Lane (not sep) and shared roadways | 2 | 2 | Condition | 4 | 4 | Add | $ 60,000 | $60,000 | NA | $ - | $ - | $ - | 3 to 5 years | $ 20,000 | $20,000 | 0 | Miles | Miles | 200 | 200 | 
19 | Geotechnical | Earth Retaining Systems (includes gravity, soil nail, soldier pile, sheet pile, reinforced concrete cantilever, MSE, crib, bin, timber, other types on the TAMS list) | Earth Retaining Systems (includes gravity, soil nail, soldier pile, sheet pile, reinforced concrete cantilever, MSE, crib, bin, timber, other types on the TAMS list) | 2 | 2 | Condition | 4 | 4 | Add | $ 800,000 | $800,000 | <1 year | $ 193,000 | $27,000 | $8,000 | 3 to 5 years | $ 188,000 | $188,000 | 2 | Walls | Walls | 2,500 | 2,500 | 
20 | Geotechnical | Reinforced Soil Slopes | Reinforced Soil Slopes | 2 | 2 | Condition | 4 | 4 | Add | $ 150,000 | $150,000 | <1 year | $ 39,000 | $39,000 | $1,000 | 3 to 5 years | $ 36,000 | $36,000 | 1 | Slopes | Slopes | 500 | 500 | 
21 | Geotechnical | Improved Ground Supports (includes column-support embankments and transfer platforms) | Improved Ground Supports (includes column-support embankments and transfer platforms) | 2 | 2 | Condition | 4 | 4 | Add | $ 30,000 | $30,000 | <1 year | $ 8,000 | $8,000 | $1,000 | 3 to 5 years | $ 5,000 | $5,000 | 1 | Support Areas | Support Areas | 100 | 100 | 
16 | Pavements | High Volume Frontage Roadway | High Volume Frontage Roadway | 2 | 2 | Cycle+ | 2 | 2 | Add | $ - | $ - | <1 year | $ 2,000 | 2,000 | $ - | NA | $ - | $ - | 0 | Centerline miles | Centerline miles | 100 | 100 | 
18 | Pavements | Highway Ramps/loops | Highway Ramps/loops | 2 | 2 | Cycle+ | 2 | 2 | Add | $ 60,000 | $60,000 | NA | $ - | $ - | $ - | 3 to 5 years | $ 20,000 | $20,000 | 0 | Centerline miles | Centerline miles | 200 | 200 | 
Total | Totals |  |  |  |  |  |  |  |  | $ 1,120,000 | $1,120,000 |  | $ 245,000 | $79,000 | $11,000 |  | $ 273,000 | $273,000 | 7 |  |  |  |  | 
Notes:   Baseline Inventory – 3 Gaps
    Active: Current Collection efforts curb ramp and sidewalk, including inspections (greater MN complete)
    Geotechnical Asset Funding allocated for MnDOT 0.5 FTE
    Frontage Roads and ADA Parking Low-Cost Effort (AMPO)
  Inventory Currency – No Gaps
  Inspection Processes – 1 Gaps
    Funding Allocated For Innovative Condition Data Collection Using NASA Sar Satellites
  Other Implementation
    Geotechnical Assets Funding Allocated for TAMS Phase 3 Enhancement

## Slide 51: Tier 2 Asset Data Collection Planning Takeaways
Fun Fact: Maplewood Lab has a Robot named husky!
“To keep the pedestrian inventory data current, this winter there is an effort to move construction inspectors from using current electronic form completion (prior to construction close-out) to a user friendly MnDOT GIS web-application (Similar to survey123) with data sorting and analysis.”
Stay The Course
Baseline Inventory <1 year (MnDOT FTE, $80K)
Inspection of Geotechnical and Ancillary Pavements 3-5 years (?, $300K)

## Slide 52: Tier 3 Asset Results Part 1
  Tier 3
    y
  Asset Groups
    Bike and Ped
    Facilities
    Geotechnical
    Hydraulic Infra
    Ancillary Pavements
    Structures
  Cycle+ and Cycle
  Maturity Gaps
 | Matrix Drivers |  |  |  |  |  | 
Asset ID | Asset Group | Asset Class | Asset Class | Tier | Desired AM Approach | AM Maturity Step Gap | 
46 | Bike and Ped | Shared use paths, side paths, sep bike lanes | Shared use paths, side paths, sep bike lanes | 3 | Cycle | 2 | 
13 | Facilities | Class 2 and 3 rest areas,Class 2 and 3 Truck Stations, Brine Buildings (S&I Operations), Weigh Stations | Class 2 and 3 rest areas,Class 2 and 3 Truck Stations, Brine Buildings (S&I Operations), Weigh Stations | 3 | Cycle+ | 0 | 
36 | Geotechnical | Instrumentation Systems (includes inclinometer, pressure cell, gauge, cabinet, and piezometer) | Instrumentation Systems (includes inclinometer, pressure cell, gauge, cabinet, and piezometer) | 3 | Cycle+ | 3 | 
48 | Geotechnical | Special Drainage Systems (includes chimney drain, perforated drain, herringbone drain, geomembrane cap and liner, and trench drain - does not include edge drains) | Special Drainage Systems (includes chimney drain, perforated drain, herringbone drain, geomembrane cap and liner, and trench drain - does not include edge drains) | 3 | Cycle | 2 | 
49 | Green Assets | Hazard - Noxious Weeds | Hazard - Noxious Weeds | 3 | Other | 0 | 
26 | Hydraulic Infra | Ponds, Infiltration Basins, and Underground Storage | Ponds, Infiltration Basins, and Underground Storage | 3 | Cycle+ | 3 | 
25 | Hydraulic Infra | Deep Stormwater Tunnels | Deep Stormwater Tunnels | 3 | Cycle+ | 0 | 
28 | Hydraulic Infra | Structual Pollution Control Devices (SPCD's) | Structual Pollution Control Devices (SPCD's) | 3 | Cycle+ | 2 | 
47 | Hydraulic Infra | Local Road Culverts | Local Road Culverts | 3 | Cycle | 2 | 
27 | Hydraulic Infra | Storm Sewer Pipe and Structures | Storm Sewer Pipe and Structures | 3 | Cycle+ | 3 | 
34 | Maintenance | Roadway Weather Information System (RWIS) | Roadway Weather Information System (RWIS) | 3 | Cycle+ | 1 | 
41 | Pavements | Paved Shoulders | Paved Shoulders | 3 | Cycle+ | 2 | 
43 | Pavements | Low Volume Frontage Roads | Low Volume Frontage Roads | 3 | Cycle+ | 2 | 
37 | Structures | Entrance Monuments | Entrance Monuments | 3 | Cycle+ | 0 | 
24 | Structures | Wood Noisewalls | Wood Noisewalls | 3 | Cycle+ | 0 | 

## Slide 53: Tier 3 Asset Results Part 2
  Asset Groups
    Traffic
  Maturity Gaps
    Signs
    Pavement Messages
    Pavement Striping
 | Matrix Drivers |  |  |  | 
Asset ID | Asset Group | Asset Class | Tier | Desired AM Approach | AM Maturity Step Gap
29 | Traffic | Sign Panels - Static | 3 | Cycle+ | 1
32 | Traffic | Sign Structures - I-beam w/Static Panel | 3 | Cycle+ | 1
33 | Traffic | Lighting - Roadway | 3 | Cycle+ | 0
30 | Traffic | Sign Structures - Static Panel Ground Mounted | 3 | Cycle+ | 1
31 | Traffic | Sign Structures - Static Panel Overheads w/Foundations | 3 | Cycle+ | 1
44 | Traffic | Pavement Markings - Messages | 3 | Cycle | 2
42 | Traffic | Barrier - Plate beam | 3 | Cycle+ | 0
38 | Traffic | Barrier - Attenuators (Crash Cushions) | 3 | Cycle+ | 0
39 | Traffic | Barrier - Plate beam End treatments | 3 | Cycle+ | 0
40 | Traffic | High Tension Cable Barrier | 3 | Cycle+ | 0
45 | Traffic | Pavement Markings - Striping | 3 | Cycle | 1

## Slide 54: Tier 3 Asset Methodology Analysis (One-Time Collect)
Gap in Asset Inventory Data Analysis
HDR Project in 2018 3,000/Project
$250K Effort
Alternative Method to Use MnDOT Resources
*These costs use historical data from one project and do not include conflation
Notes: Access Database
Gaps where we didn’t get as-builts
HDR project 3,000/project

## Slide 55: Tier 3 Methodology Analysis (Annual Collect)
MnDOT Signs are replaced by 3 methods
  1. Maintenance Damage Repairs
  2. Maintenance and Contractor Annual Sign Replacement Projects
    Lower Cost For Comparison Purposes (5 min/sign)
    25,000 signs (15-year life cycle)
    1.0 FTE or $150,000
  3. Construction Project Impacts
    Annual 2-5% of Sign Modifications
    As-built $13/sign cost in 2019
    $150-$200,000
District 3 Pilot Project Mobile Lidar & Conflation $3.50/sign.
  Mobile Lidar Cyclical Collect $150K/Year
  Reduced MnDOT Staff Time

## Slide 56: Tier 3 Methodology Analysis (Annual Collect)
  Above Ground Assets
    Traffic Barrier
    Concrete Barrier
    Rumbles
    Signs
    Noisewalls
  Economies of Scale
  High-level Cost Exercise
  Concrete Barrier $65 each Versus $13/Pt As-Builts

## Slide 57: Tier 3 Asset Results – Stay The Course

## Slide 58: Tier 3 Asset Data Collection Planning - Add
 | Matrix Drivers |  |  |  |  |  | Plan summary |  | Baseline Inventory |  | Inv. Currency | Condition Inventory |  | System standup |  |  | 
Asset ID | Asset Group | Asset Class | Asset Class | Tier | Desired AM Approach | AM Maturity Step Gap | Short Description | 5 year Plan Sub-total ($10k resolution) | Timeline To Complete Inventory | Inventory Baseline Cost Estimate | Inventory Currency Annual Cost Estimate | Timeline To Complete Inspection Cycle | Inspection Plan - Annual Cost Estimate (Baseline incl.) | Other Imp. Tasks | Strategic Asset Unit | Statewide Count | 
46 | Bike and Ped | Shared use paths, side paths, sep bike lanes | Shared use paths, side paths, sep bike lanes | 3 | Cycle | 2 | Add | $ 160,000 | NA | $ - | $ 20,000 | 3 to 5 years | $ 20,000 | 2 | Miles | 200 | 
36 | Geotechnical | Instrumentation Systems (includes inclinometer, pressure cell, gauge, cabinet, and piezometer) | Instrumentation Systems (includes inclinometer, pressure cell, gauge, cabinet, and piezometer) | 3 | Cycle+ | 3 | Add | $ 50,000 | <1 year | $ - | $ 1,000 | 3 to 5 years | $ 15,000 | 1 | Systems | 30 | 
48 | Geotechnical | Special Drainage Systems (includes chimney drain, perforated drain, herringbone drain, geomembrane cap and liner, and trench drain - does not include edge drains) | Special Drainage Systems (includes chimney drain, perforated drain, herringbone drain, geomembrane cap and liner, and trench drain - does not include edge drains) | 3 | Cycle | 2 | Add | $ 10,000 | <1 year | $ 3,000 | $ 1,000 | 3 to 5 years | $ - | 2 | Pipes | 250 | 
26 | Hydraulic Infra | Ponds, Infiltration Basins, and Underground Storage | Ponds, Infiltration Basins, and Underground Storage | 3 | Cycle+ | 3 | Add | $ 370,000 | 1 to 3 years | $ 50,000 | $ 25,000 | 1 to 3 years | $ 65,000 | 0 | Ponds | 1,300 | 
28 | Hydraulic Infra | Structual Pollution Control Devices (SPCD's) | Structual Pollution Control Devices (SPCD's) | 3 | Cycle+ | 2 | Add | $ 50,000 | 1 to 3 years | $ 25,000 | $ - | 1 to 3 years | $ 9,000 | 0 | Structures | 86 | 
47 | Hydraulic Infra | Local Road Culverts | Local Road Culverts | 3 | Cycle | 2 | Add | $1,140,000 | 3 to 5 years | $ 720,000 | $ 12,000 | 3 to 5 years | $ 121,000 | 0 | Pipes | 12,093 | 
27 | Hydraulic Infra | Storm Sewer Pipe and Structures | Storm Sewer Pipe and Structures | 3 | Cycle+ | 3 | Add | $11,010,000 | <1 year | $ 75,000 | $ 168,000 | > 5 years | $ 3,366,000 | 0 | Pipe/Structures | 168,285 | 
Notes:   Baseline Inventory – X Gaps
    Active:
  Inventory Currency – Y Gaps
  Inspection Processes – Z Gaps
    f
  Other Implementation
    EE
Clarify storm sewer plans – what are we actually adding

## Slide 59: Tier 3 Asset Data Collection Planning - Add
 | Matrix Drivers |  |  |  |  | Plan summary |  | Baseline Inventory |  | Inv. Currency | Condition Inventory |  | System standup |  |  | 
Asset ID | Asset Group | Asset Class | Tier | Desired AM Approach | AM Maturity Step Gap | Short Description | 5 year Plan Sub-total ($10k resolution) | Timeline To Complete Inventory | Inventory Baseline Cost Estimate | Inventory Currency Annual Cost Estimate | Timeline To Complete Inspection Cycle | Inspection Plan - Annual Cost Estimate (Baseline incl.) | Other Imp. Tasks | Strategic Asset Unit | Statewide Count | 
29 | Traffic | Sign Panels - Static | 3 | Cycle+ | 1 | Add | $ 2,230,000 | 1 to 3 years | $ 750,000 | $ 80,000 | 3 to 5 years | $ 359,000 | 0 | Panels | 430,262 | 
32 | Traffic | Sign Structures - I-beam w/Static Panel | 3 | Cycle+ | 1 | Add | $ 220,000 | 1 to 3 years | $ 63,000 | $ 1,000 | 3 to 3 years | $ 50,000 | 0 | Supports | 2,510 | 
33 | Traffic | Lighting - Roadway | 3 | Cycle+ | 0 | Add | $ 2,200,000 | 3 to 5 years | $ 150,000 | $ 85,000 | 3 to 5 years | $ 543,000 | 2 | Lighting units | 27,147 | 
44 | Traffic | Pavement Markings - Messages | 3 | Cycle | 2 | Add | $ 1,100,000 | 3 to 5 years | $ 350,000 | $ 150,000 | NA | $ - | 1 | Markings | 100,000 | 
38 | Traffic | Barrier - Attenuators (Crash Cushions) | 3 | Cycle+ | 0 | Add | $ 340,000 | <1 year | $ 30,000 | $ 1,000 | NA | $ 100,000 | 1 | Barriers | 2,493 | 
39 | Traffic | Barrier - Plate beam End treatments | 3 | Cycle+ | 0 | Add | $ 2,300,000 | <1 year | $ 30,000 | $ 75,000 | NA | $ 633,000 | 0 | Barriers | 15,828 | 
40 | Traffic | High Tension Cable Barrier | 3 | Cycle+ | 0 | Add | $ 170,000 | <1 year | $ 60,000 | $ 5,000 | NA | $ 29,000 | 0 | Miles | 722 | 
45 | Traffic | Pavement Markings - Striping | 3 | Cycle | 1 | Add | $ 520,000 | <1 year | $ 20,000 | $ 100,000 | NA | $ - | 0 | Miles | 45,224 | 
Total | Totals |  |  |  |  |  | $22,040,000 |  | $ 2,326,000 | $ 725,000 |  | $ 5,366,000 | 10 |  |  | 
Notes:   Baseline Inventory – X Gaps
    Active:
  Inventory Currency – Y Gaps
  Inspection Processes – Z Gaps
    f
  Other Implementation
    EE
Big add is total sign collect remaining districts if done

## Slide 60: Tier 3 Asset Data Collection Planning Key Takeaways
Geotechnical Inventory (MnDOT, $75K)
Hydraulic Inventories (MnDOT, $XK)
Sign Inventory Baseline Need in Four Districts (Consultant, $1.2M)
Multiple Asset Inventory One-Time Project (Consultant, $250K)
Inspections on Multiple Assets ($5M Annual, 3 to 5 Years)
Fun Facts:
Research Bike From Park & Trails Council Collects
Data Used To Rate Trail Conditions.

## Slide 61: Tier 4 Asset Results
  Tier 4
    Inventory
    Only Inspection of Snow Fence
  Asset Groups
    Maintenance
    Green
    Facilities
    Geotechnical
    ROW
    Traffic
  Cycle+, Reactive
  Maturity Gaps
 | Matrix Drivers |  |  |  |  | 
Asset ID | Asset Group | Asset Class | Tier | Desired AM Approach | AM Maturity Step Gap | 
58 | Maintenance | Snow Fence (Types: Living, Structural, Grading) | 4 | Cycle+ | 2 | 
59 | Green Assets | Native/Pollinator Plantings | 4 | Other | 0 | 
14 | Facilities | Storage sheds, and misc. buildings (lift stations, hazmat, etc.) | 4 | Reactive | 0 | 
51 | Geotechnical | Natural Hazard Locations (includes locations off of the ROW not otherwise addressed) | 4 | Reactive | 1 | 
52 | Geotechnical | Improved Subgrade Fills (includes lightweight fill such as: wood chip, tire-derived aggregate, geofoam, lightweight aggregate, cellular concrete, and grouted fill) | 4 | Reactive | 1 | 
53 | Green Assets | Replacement Wetlands | 4 | Reactive | 1 | 
54 | Green Assets | Trees (Types: Historic, Notable, High-Risk, Land Bearing) | 4 | Reactive | 1 | 
55 | Right of Way | Land, Boundary, Excess or Surplus Right of Way | 4 | Reactive | 0 | 
50 | Structures | Concrete Noise | 4 | Reactive | 0 | 
56 | Traffic | Concrete Barrier | 4 | Reactive | 0 | 
57 | Traffic | Rumble Strips and Stripes | 4 | Reactive | 1 | 

## Slide 62: Tier 4 Asset Results Data Collection Planning – Stay the Course
Notes:   Baseline Inventory – 5 Gaps, Active:
  Inventory Currency – No Gaps, Adding Snow Fence to As-builts or get data from Design
  Inspection Processes – 1 Gap, future Snow Fence Inspection
  Other Implementation Tasks, 4 -

## Slide 63: Tier 4 Asset Results Data Collection Planning - Add
 | Matrix Drivers |  |  |  |  |  | Plan summary |  | Baseline Inventory |  | Inv. Currency | Condition Inventory |  | System standup |  |  | 
Asset ID | Asset Group | Asset Class | Asset Class | Tier | Desired AM Approach | AM Maturity Step Gap | Short Description | 5-year Plan Sub-total ($10k resolution) | Timeline To Complete Inventory | Inventory Baseline Cost Estimate | Inventory Currency Annual Cost Estimate | Timeline To Complete Inspection Cycle | Inspection Plan - Annual Cost Estimate (Baseline incl.) | Other Imp. Tasks | Strategic Asset Unit | Statewide Count | 
58 | Maintenance | Snow Fence (Types: Living, Structural, Grading) | Snow Fence (Types: Living, Structural, Grading) | 4 | Cycle+ | 2 | Add | $180,000 | <1 year | $5,000 | $10,000 | 3 to 5 years | $40,000 | 2 | Fences/Traps | 200 | 
51 | Geotechnical | Natural Hazard Locations (includes locations off of the ROW not otherwise addressed) | Natural Hazard Locations (includes locations off the ROW not otherwise addressed) | 4 | Reactive | 1 | Add | $70,000 | 1 to 3 years | $67,000 | $1,000 | NA | $ - | 1 | Centroids | 1,000 | 
52 | Geotechnical | Improved Subgrade Fills (includes lightweight fill such as: wood chip, tire-derived aggregate, geofoam, lightweight aggregate, cellular concrete, and grouted fill) | Improved Subgrade Fills (includes lightweight fill such as: wood chip, tire-derived aggregate, geofoam, lightweight aggregate, cellular concrete, and grouted fill) | 4 | Reactive | 1 | Add | $20,000 | 1 to 3 years | $13,000 | $1,000 | NA | $ - | 1 | Fill Areas | 200 | 
53 | Green Assets | Replacement Wetlands | Replacement Wetlands | 4 | Reactive | 1 | Add | $10,000 | 1 to 3 years | $7,000 | $ - | NA | $ - | 0 | Wetland areas | 15 | 
57 | Traffic | Rumble Strips and Stripes | Rumble Strips and Stripes | 4 | Reactive | 1 | Add | $460,000 | 1 to 3 years | $8,000 | $90,000 | NA | $ - | 0 | Miles | 12,000 | 
Total | Totals |  |  |  |  |  |  | $740,000 |  | $100,000 | $102,000 |  | $ 40,000 | 4 |  |  | 
Notes:   Baseline Inventory – 5 Gaps, Active:
  Inventory Currency – No Gaps, Adding Snow Fence to As-builts or get data from Design
  Inspection Processes – 1 Gap, future Snow Fence Inspection
  Other Implementation Tasks, 4 -

## Slide 64: Tier 4 Asset Data Collection Planning Key Takeaways
Snow Fence Inventory Updates From 2016-2020 (MnDOT, 1-3 Years)
Geotechnical Assets (MnDOT, <1 Year)
Updates from Paper to GIS Wetland Replacement (MnDOT, 3-5 years)
Future Inspection of Snow Fence (?, 3-5 years)
Fun Facts:
Snow Fence Collector Application Will be the Foundation for the “Farmer to Farmer Snow Fence Networking web-site.

## Slide 65: Pivot Graphs
Chart: AM Gap per Tier
| 0 | 1 | 0 | 3 | 4 | 0 | 1 | 2 | 3 | 0 | 1 | 2 | 1 | 2 | 3 | 4
Total | 6 | 1 | 4 | 3 | 6 | 12 | 6 | 5 | 3 | 5 | 5 | 1
Chart: Sum of AM Gap Steps by MnSHIP Category
| Roadside Infra | Pavement Condition | Accessible Ped Infra | <null> | Bycycle Infra | Traveler Safety | Project Delivery | Bridge Condition | (blank) | Facilities | NA
Total | 32 | 10 | 8 | 6 | 6 | 4 | 1 | 0 | 0 | 0 | 0
Notes:   Maturity Gaps
  Baseline Inventory – X Gaps
    Active:
  Inventory Currency – Y Gaps
  Inspection Processes – Z Gaps
    f
  Other Implementation
    EE

## Slide 66: Trivia Time Please Type Your Answer In The Chat Box
Be The First To Answer….
  How

## Slide 67: Recommendations
DAVE Solsrud

## Slide 68: Recommendation A
Move Forward with MnDOT Resource Low-Cost Efforts
  GIS Frontage Road Inventory (Metro AM)
  Metro District Concrete Barrier Conflation (Metro AM)
  Catch Basin Lidar Conflation (AMPO/Districts)
  Light Pole and Signal Pole Lidar Conflation (AMPO/ESS/Districts)
  Replacement Wetland GIS Inventory (OLM)
  Mowing Inventory For Performance Measures (AMPO)
  Accessible ADA Parking Inventory
  Snow Fence Inventory
Each Effort Estimated to Cost Less Than $25,000

## Slide 69: Recommendation B
Obtain full District inventory of structural pollution control devices (SPCD), ponds and basins using MnDOT resources and with input/review from Districts.
Definitions
Highway Culverts: In place culverts with a roadway type of centerline, collector/distributor, mainline, media, ramp/loop or roundabout
Local Road Culverts: In place culverts with a roadway type of city, county, frontage
Entrance Culverts: In place culverts with a roadway type of entrance, farm entrance, field entrance, commercial entrance
Flume: Pipe that conveys water down a steep slope, energy may be dissipated in the pipe flume itself and/or at the outlet
Estimated Time Commitment of 6 months GIS Analyst and 4 Weeks of District Review.
Notes: Comments:
Current practice in some Districts already
Advance 081 efforts
Legal and Operational Risks

## Slide 70: Recommendation C
Program One-Time Consultant Project To Conflate Asset Traffic Barrier, Rumbles, and Striping Inventories Impacted By 2019 and 2020 Construction Seasons.
Existing HDR project yielded $3,000/project
Notes: HDR 3,000 per project yield cost of roughly $250,000

## Slide 71: Recommendation D
Not Inventorying
  Fence
  Edge Drains
  Ditches
  Curb and Gutter
  Unimproved Subgrade
  Cut Slopes
  Gravel Shoulders
  Embankments
These Asset Were Recognized as Minimum Maintenance Assets & Asset Inventories Not Required

## Slide 72: Recommendation E
We recommend including all below ground assets in SRC as-builts 2011.601.
  Electrical Systems (For Example, Lights, Signals, ITS, Weigh Stations)
  All culvert types (highway, local road and entrance).
  Storm drainpipes and catch basins.
Definitions
Highway Culverts: In place culverts with a roadway type of centerline, collector/distributor, mainline, media, ramp/loop or roundabout
Local Road Culverts: In place culverts with a roadway type of city, county, frontage
Entrance Culverts: In place culverts with a roadway type of entrance, farm entrance, field entrance, commercial entrance
Flume: Pipe that conveys water down a steep slope, energy may be dissipated in the pipe flume itself and/or at the outlet
Notes: Comments:
Law requirement for Gopher State One Call
Streamlining review and import methodology through AMPO/District staff

## Slide 73: Recommendation F
Upgrade Automated Vehicle Location Data Logging Systems on Central Office Stripers and Integrate Data with TAMS
Estimate From The Vendor of $70,000 For Equipment and Estimate of IT Time ~$30K
Notes: Comments:
Means to Document Material Type
Current System is Desperate
Efficient
New System Designed For TAMS Integration

## Slide 74: Recommendation G
Program A Statewide Annual Mobile Lidar Collection Project Each Fall To Update Construction Project Data (Signs and Several Other Above Ground Assets).

## Slide 75: Recommendation H
Inspections
  Storm sewer inspection will take place during the scoping process and added throughout time.
  Structural pollution control devices (SPCD), ponds and basins Inspection cycle to be determined by current requirements from permits, MS4 SWPPP or District needs.
Definitions
Highway Culverts: In place culverts with a roadway type of centerline, collector/distributor, mainline, media, ramp/loop or roundabout
Local Road Culverts: In place culverts with a roadway type of city, county, frontage
Entrance Culverts: In place culverts with a roadway type of entrance, farm entrance, field entrance, commercial entrance
Flume: Pipe that conveys water down a steep slope, energy may be dissipated in the pipe flume itself and/or at the outlet
Notes: Comments:
Building asset inventory for Gopher State One Call
One-time storm sewer inventory would be expensive and time consuming
Strategy becomes building the inventory over-time
Right time for inspection data

## Slide 76: Recommendation I
Interoperable Design, Construction, and Asset Management Software Systems (data) Forming a Whole Lifecycle Approach
  For Example, Provide Training and Support on The New Transportation Asset Management Based Sign Inventory Design Plan Data Table Template.

## Slide 77: Recommendation J
Conduct Data Inter-relationship and Data Value Pilot
  Pick 1 or 2 Assets
  Understand Current Efforts
    What Data Collected When
    How Much Attribution
    Are Districts Using The Data
  Streamline Future Efforts
    Maximize Data Sharing From Concept – Plan – Scope – Design – Construction - Manage
    Set Expectations For Level of Attribution At Each Phase
  Communicate Results

## Slide 78: Recommendation K
Reduce MnDOT Data Collection Efforts
  Maintenance Snow and Ice Labor, Equipment, Material (LEM) Data Entry into RCA. TAMS and MDSS Integration Project.
  Sign Maintenance Data Entry for Sign Replacement Projects
  As-built Processing For Signs, Noise Walls, and Traffic Barrier (annual LiDAR)
  Sign Design Plan Development (New Template)
“
When employed correctly, four ounces can move a
thousand pounds
“
-Mulan
Notes: When employed correctly, four ounces can move a thousand pounds. - Mulan

## Slide 80
Attractive Roadsides
Mowing Maps
Snow & Ice
Analysis & Reporting
Smooth Pavement Pavement Van Analysis
Drainage
TAMS Development & Support
Roadside Safety
Traffic Barrier Mapbooks
Fleet
AVL Analysis
Structures
Inspections and Reporting
ADA Data Collection
Damage Restitution Contract Updates
District
As-Built Experts
Maintenance
GIS Mapping
Summer Work Plan
Work Planning

## Slide 82: Active Efforts

## Slide 83: Active Efforts to Update Baseline Inventory
Signals and Lighting Inventory Updates from 2018 LiDAR data
Pedestrian Infrastructure Sidewalk and Curb Ramps ($1M)
Mowing Inventory for Performance Measures

## Slide 84: TAMS Phase 3
Build Window(s) for Snow Fence Inventory and Inspection
Build Window(s) for Entrance Monument Inventory
Pavement Long-Lines and Message Modifications and App
Lighting Inventory and Inspection Application
Signal Inventory and Inspection Application
Overhead Sign Structure Inspection Application